## Slide 1
Eleven Primitives and Three Gates:
The Universal Structure of Computational Imaging
Chengshuai Yang, David J. Brady, Xin Yuan
NextGen PlatformAI C Corp | University of Arizona | Westlake University
Talk for Prof. Yuan's Group | March 2026
1/30

## Slide 2
Talk Outline
~40 minutes
1. Motivation: Why do reconstruction algorithms fail on real instruments?
2. Key Idea: 11 primitives + 3 gates = universal grammar
3. The Finite Primitive Basis Theorem (Theorem 1)
- OperatorGraph representation
- 11 canonical primitives
- Basis-growth saturation
4. The Triad Decomposition (Theorem 2)
- Three gates: Recoverability, Carrier Budget, Operator Mismatch
- Four-Scenario evaluation protocol
5. Experimental Validation (12 modalities, 5 carrier families)
- CASSI deep dive + hardware validation
- Cross-carrier results: CT, MRI, cryo-EM, ultrasound
6. Discussion and Future Directions
2/30

## Slide 3
The Problem: Silent Reconstruction Failure
Computational imaging has made enormous progress in algorithms:
- Compressed sensing, Plug-and-Play, deep unrolling, vision transformers...
But algorithms routinely fail on deployed instruments.
The root cause is often NOT the algorithm --- it's the forward model.
When the assumed operator H_nom differs from the true physics H_true,
the solver faithfully solves the WRONG problem.
This failure is silent and systematic:
- Produces structured artifacts that mimic signal content
- Practitioners blame the solver, not the model
- No general framework to diagnose or fix it
3/30

## Slide 4
Diverse Systems, Shared Structure
A coded-aperture camera, an MRI scanner, and a cryo-electron microscope
appear to share nothing: different carriers, geometries, detectors.
Yet each converts a physical scene into measurements by composing
a small chain of transformations:
propagation -> interaction -> encoding -> detection
Key insight: This universality is not accidental --- it reflects the
finite structure of physical measurement processes.
Question: Can we formalize this?
- What are the minimal building blocks?
- Why do reconstructions fail, and how to diagnose them?
4/30

## Slide 5
Our Answer: 11 Primitives + 3 Gates
A universal grammar for computational imaging
Theorem 1: Finite Primitive Basis
Every imaging forward model decomposes
into a DAG over exactly 11 primitives.
Sufficient + Minimal basis.
Covers all 5 carrier families.
170 modalities validated.
Theorem 2: Triad Decomposition
Every reconstruction failure has exactly
3 independent root causes (gates):
Gate 1: Information deficiency
Gate 2: Carrier noise
Gate 3: Operator mismatch
Together: a compositional language for designing, diagnosing, and correcting ANY imaging system.
Validation: 12 modalities, 5 carrier families, +0.8 to +13.9 dB recovery on real instruments.
5/30

## Slide 6
Figure 1: The Universal Grammar of Computational Imaging
6/30

## Slide 7
PART I
The Finite Primitive Basis
Every imaging forward model decomposes into a DAG over exactly 11 primitives
7/30

## Slide 8
The OperatorGraph Representation
Every imaging forward model encoded as a typed DAG:
- Each node wraps a single primitive physical operator
- Edges define data flow from source to detector
Every primitive implements:
- forward(x) -> y (physics simulation)
- adjoint(y) -> x (validated: <Hx,y> = <x,H*y>)
Key properties:
- Adjoint consistency: randomized dot-product test, delta < 10^-6
- Lipschitz bounds: nonlinear primitives restricted to 5 canonical families
- Not a universal approximator (unlike neural networks)
This makes reconstruction both interpretable and certifiable.
8/30

## Slide 9
The 11 Canonical Primitives
# Primitive Notation Physical Action
1 Propagate P(d, lambda) Free-space wave propagation
2 Modulate M(m) Element-wise multiplication (mask, coil, absorption)
3 Project Pi(theta) Radon line-integral projection
4 Encode F(k) Fourier-domain encoding (k-space)
5 Convolve C(h) Spatial convolution (PSF)
6 Accumulate Sigma Summation over spectral/temporal axis
7 Detect D(g, eta) Detector response (5 canonical families)
8 Sample S(Omega) Sub-sampling on index set
9 Disperse W(alpha, a) Wavelength-dependent spatial shift
10 Scatter R(sigma, dE) Direction change and/or energy shift
11 Transform Lambda(f, theta) Pointwise nonlinear physics operation
9 linear primitives (have adjoint) + 2 nonlinear (Detect, Transform)
Detect: 5 families (linear-field, log, sigmoid, intensity |x|^2, coherent) -- max 2 params each
Transform: 5 families (Beer-Lambert, log, phase wrap, polynomial, saturation) -- bounded Lipschitz
9/30

## Slide 10
Figure 2: OperatorGraph DAGs + Fidelity Ladder + Basis Growth
10/30

## Slide 11
Example DAG Decompositions
CASSI (photon): M -> W -> Sigma -> D (4 nodes, depth 4)
mask * disperse * sum_spectral * detect
CT (X-ray): Pi -> D (2 nodes, depth 2)
radon_project * detect
MRI (nuclear spin): M -> F -> S -> D (4 nodes, depth 4)
coil_modulate * fourier_encode * k-space_sample * detect
Ptychography (e-): M -> P -> D (3 nodes, depth 3)
probe_modulate * fresnel_propagate * detect
Ultrasound: P -> Sigma -> D (3 nodes, depth 3)
wave_propagate * delay_sum * detect
Median: 3 nodes, depth 3. Max observed: 5 nodes, depth 5.
Theoretical bounds: N_max = 20, D_max = 10 (very conservative).
11/30

## Slide 12
Theorem 1: Finite Primitive Basis
For every H in C_img (the imaging operator class),
there exists a typed DAG G with nodes from B = {P, M, Pi, F, C, Sigma, D, S, W, R, Lambda}
that is an epsilon-approximate representation of H.
The library B has exactly 11 elements and is minimal:
removing any primitive leaves at least one modality with error > epsilon.
Proof sketch:
1. H = H_K ... H_1 with K <= N_max stages
2. Each stage classified into 6 physics families
3. Each family mapped to 1-2 primitives
4. Linear composition: sub-multiplicative error ||H - H_G|| <= K * max(eps_k) * B^(K-1)
5. Nonlinear: Lipschitz bound ||H(x) - H_G(x)|| <= sum eps_k * prod gamma_j
Minimality: 8 primitives strictly necessary; 3 more needed under complexity bounds.
Witness modality for each removal (e.g., without Pi, CT has e_img >> 0.01).
12/30

## Slide 13
Decomposition Results: All e_img < 0.01
Full-validation modalities (12 with 4-scenario correction):
CASSI (photon): M->W->Sigma->D e < 10^-4
CACTI (photon): M->Sigma->D e < 10^-4
CT (X-ray): Pi->D e < 10^-5
MRI (spin): M->F->S->D e < 10^-6
Ptychography (e-): M->P->D e = 4.2x10^-4
+ 7 more modalities (lensless, SPC, fluorescence, holography, CBCT, cryo-EM, ultrasound)
Held-out modalities (frozen library, 0 new primitives):
OCT, photoacoustic, SIM, phase-contrast X-ray, electron ptychography
All pass: e_img < 0.01
Exotic modalities:
Ghost imaging, THz-TDS, Compton*, Raman, fluorescence, DOT, Brillouin
*Compton triggered extension protocol: e=0.34 without Scatter R -> e<0.01 with R
13/30

## Slide 14
Basis-Growth Saturation: K=11 Suffices
9 of 11 primitives introduced by
first 10 modalities
K = 11 at N = 35 modalities
No new primitive for next 135
Sublinear, saturating growth:
New modalities compose existing
primitives rather than requiring
new ones
Consistent with theorem:
Once all 6 physics-stage families
are covered, basis is complete.
14/30

## Slide 15
PART II
The Triad Decomposition
Every reconstruction failure has exactly 3 independent root causes
15/30

## Slide 16
Why Exactly Three Gates?
The reconstruction pipeline has exactly 3 inputs:
1. A sensing geometry H --> determines what information is captured
2. A physical carrier --> determines the noise floor
3. A forward model H_nom --> what the solver inverts
Any reconstruction error must trace to one of these:
Gate 1: Information never captured (null space of H)
Gate 2: Information captured but corrupted (carrier noise)
Gate 3: Information captured but misinterpreted (H_nom != H_true)
This trichotomy is exhaustive:
MSE <= MSE^(G1) + MSE^(G2) + MSE^(G3) (no residual term)
Solver suboptimality is subsumed by Gate 3 (solver's implicit model).
16/30

## Slide 17
The Three Gates in Detail
Gate 1: Recoverability
Is enough information
captured?
Compression ratio gamma=m/n
Null space dimension
PSNR ceiling from theory
Fix: acquire more data
Gate 2: Carrier Budget
Is the SNR sufficient?
Shot noise (photon counting)
Thermal noise (electronic)
T1/T2 relaxation (MRI)
Fix: source/detector
improvement
Gate 3: Operator Mismatch
Does H_nom match H_true?
Geometric misalignment
Parameter drift
Model simplification
Fix: calibration /
operator correction
Key Insight: Gate 3 dominates in well-designed instruments
Gates 1 & 2 are addressed at design time (sampling geometry, carrier selection).
Gate 3 (operator mismatch) is the deployment-stage bottleneck: 14/14 configurations show Gate 3 dominant.
This is why algorithms often fail on real instruments: the model is wrong, not the solver.
The Triad tells you WHERE the error is, and WHAT to fix.
17/30

## Slide 18
Figure 3: Triad Decomposition Validated Across All Carriers
18/30

## Slide 19
Evaluation: The Four-Scenario Protocol
Every modality evaluated under 4 standardized scenarios:
Scenario I (Ideal): y = H_true * x, reconstruct with H_true
--> Oracle upper bound. Best possible quality.
Scenario II (Mismatch): y = H_true * x, reconstruct with H_nom (H_nom != H_true)
--> Standard operating condition. The model is WRONG.
Scenario III (Oracle): Same y as Sc. II, reconstruct with H_true
--> Correction ceiling. What's achievable if you knew the truth.
Scenario IV (Corrected): Same y as Sc. II, reconstruct with H_hat (estimated)
--> Our contribution. Autonomous calibration recovers quality.
Recovery ratio: rho = (PSNR_IV - PSNR_II) / (PSNR_I - PSNR_II)
rho=0: calibration useless. rho=1: fully closes the gap.
19/30

## Slide 20
PART III
Experimental Results
12 modalities, 5 carrier families, +0.8 to +13.9 dB recovery
20/30

## Slide 21
Figure 4: Correction Results Across 14 Configurations
14 configurations across 5 carriers:
Optical photons:
CASSI: +6.68 dB (10 scenes)
CACTI: +4.37 dB (6 videos)
SPC: +2.31 dB (11 images)
Lensless: +13.9 dB
Holography: +7.41 dB
Fluorescence: +0.80 dB
X-ray: CT +3.10 dB, CBCT +5.0 dB
Electron: Ptycho +6.77 dB, Cryo +2.4 dB
Spin: MRI +2.5 dB
Acoustic: Ultrasound +1.8 dB
Gate 3 dominant in ALL 14/14 cases!
21/30

## Slide 22
CASSI Deep Dive: Coded Aperture Spectral Imaging
CASSI forward model: M(mask) -> W(dispersion) -> Sigma(spectral sum) -> D(detect)
5-parameter mismatch model:
(dx, dy, theta, a1, alpha) = spatial shifts + rotation + dispersion slope + axis angle
True values: dx=0.5 px, dy=0.3 px, theta=0.1 deg, a1=2.02, alpha=0.15 deg
Correction algorithms:
Algorithm 1: Hierarchical beam search (~300s/scene)
1D sweeps -> 3D beam search -> 2D beam search -> coordinate descent
Accuracy: +/-0.1-0.2 pixels
Algorithm 2: Joint gradient refinement (~3200s/scene)
Differentiable forward model + Adam optimizer + multi-start
Accuracy: +/-0.05-0.1 pixels (3-5x improvement)
Both are SOLVER-AGNOSTIC: corrected operator benefits any downstream solver
(TwIST, GAP-TV, DGSMP, MST-L, CST-L) without retraining!
22/30

## Slide 23
Figure 5: CASSI Results + Hardware Validation
23/30

## Slide 24
Cross-Carrier Validation: 5 Carrier Families
OPTICAL PHOTONS (6 modalities):
CASSI: Sc.II = 27.63 dB -> Sc.IV = 34.31 dB (recovery ratio 0.95)
CACTI: +4.37 dB correction, EfficientSCI solver
SPC: 3 compression ratios (10%, 25%, 50%), exponential gain drift
X-RAY PHOTONS (2 modalities):
CT: center-of-rotation offset correction, FBP + SART solvers
CBCT: detector offset, 5 real images (LoDoPaB-CT, FIPS, HTC)
ELECTRONS (2 modalities):
Ptychography: probe position jitter correction via ePIE
Cryo-EM: defocus error correction, CTF-based Wiener filtering
NUCLEAR SPINS (1 modality):
MRI: coil sensitivity error correction, ESPIRiT calibration adopted
ACOUSTIC WAVES (1 modality):
Ultrasound: speed-of-sound error correction, delay-and-sum beamforming
24/30

## Slide 25
Figure 6: Cross-Carrier Zero-Shot Generalization
25/30

## Slide 26
Figure 8: Visual Comparison Across All Scenarios
26/30

## Slide 27
Key Property: Solver-Agnostic Correction
Critical distinction from previous work:
Traditional approach: Fix the algorithm (better solver, more training data)
Our approach: Fix the operator (calibrate H_nom -> H_true)
The corrected operator benefits ANY downstream solver:
- TwIST, GAP-TV (optimization-based)
- DGSMP, MST-L, CST-L, HDNet (deep learning)
- All improve without retraining!
Why this matters:
- Solver design and operator correction are orthogonal
- Better solvers + better operators = compounding gains
- One calibration serves the entire solver ecosystem
Relationship to Prof. Yuan's SCI work:
- The SCI framework unifies coded-aperture modalities
- Our 11 primitives provide the structural explanation of why SCI works
- Gate 3 analysis extends SCI to deployment-stage robustness
27/30

## Slide 28
Discussion and Broader Impact
What this paper establishes:
1. Universal structure: 11 primitives cover 170+ modalities (all 5 carrier families)
2. Complete diagnosis: 3 gates exhaust all root causes of reconstruction failure
3. Actionable correction: +0.8 to +13.9 dB on 12 validated modalities
Relationship to existing work:
- Not a better solver: COMSOL/FEniCS solve single problems better
- Complementary: fixes the operator so that ANY solver works better
- Extends SCI (Yuan et al.) from optical to all 5 carrier families
Generalization beyond imaging:
- Seismology: wave propagation + attenuation + sensor response
- Radio astronomy: aperture synthesis + ionospheric distortion + noise
- Particle physics: interaction model + detector response + pile-up
- All exhibit the same 3-gate failure structure
Limitation: formal proof in companion paper [yang2026fpt]
28/30

## Slide 29
Summary
11 Primitives (Theorem 1):
Every imaging forward model = DAG over 11 primitives
Minimal, sufficient, covers 170 modalities
Basis-growth saturates at K=11
3 Gates (Theorem 2):
Every failure = G1 (info) + G2 (noise) + G3 (mismatch)
Gate 3 dominates in deployed instruments (14/14)
Autonomous correction: +0.8 to +13.9 dB
Key Numbers:
- 11 primitives, minimal and sufficient
- 3 gates, exhaustive decomposition (MSE = MSE_G1 + MSE_G2 + MSE_G3)
- 170 modality templates, 5 carrier families
- 12 modalities with full 4-scenario validation (including 2 Nobel Prize techniques)
- +0.8 to +13.9 dB recovery on deployed instruments
- Gate 3 dominant in 14/14 validated configurations (100%)
- Solver-agnostic: one calibration benefits all downstream solvers
The first universal grammar for designing, diagnosing, and correcting
computational imaging systems.
29/30

## Slide 30
Thank You!
Questions & Discussion
Chengshuai Yang | integrityyang@gmail.com
Code: github.com/integritynoble/Physics_World_Model
Acknowledgments: Prof. David Brady (U. Arizona), Prof. Xin Yuan (Westlake)
30/30